State of Israel

The Energy Sources Regulations (Maximum Electric Output in Standby Mode for Domestic and Office Electric Appliances), 5771-2011*

By the power vested in me pursuant to Section 3 of the Energy Sources Law, 5750-1989 and with the approval of the Economic Committee of the Knesset, I hereby declare the following regulations:

1.	Herein -

“Electric output in standby mode” – the electric output measured while the instruments are not operating but remain connected to the electricity mains for an undefined time to allow for reactivation by remote control or other measures, or an electric output that is measured for the purpose of display of information on an electronic display, including a clock;

“The Standards Institution” – an institution as defined in Section 2 of the Standards Law, 5713-1953 (hereinafter – the Standards Law);

“Appliances” – electric appliances for domestic and office uses, as elaborated in the first addendum, operating at a voltage that does not exceed 230 volts and powered by connection to the electricity mains only;

“Approved laboratory” – as defined in Section 12 of the Standards Law;

“Standard” – Israeli Standard SI 62301 “domestic electrical appliances: measurement of output in standby mode” as valid from time to time in accordance with the Standards Law, a copy of which is deposited for public inspection at the offices of the Standards Institution of Israel, a link to which may be found on the website of the Ministry of National Infrastructures at the address www.mni.gov.il ; in the absence of such a link, the standard concerning these Regulations will not be valid:

2.	No person shall import, manufacture for use in Israel or sell appliances unless the Standards Institution or an approved laboratory has tested the compliance of these appliances with the Standard, and in accordance with the test, the electrical output does not exceed the maximum electrical output stipulated in the Second Addendum.

3.	A manufacturer or importer of the appliance shall provide the Commissioner information on the energy consumption of appliances in standby mode that it imports or manufactures upon the demand of the Commissioner.

4.	These Regulations take effect on 6th of Tevet, 5771 (January 1, 2012).

5.	If the standard does not state that the maximum electrical output in standby mode is as set forth in the second addendum, no person shall import, manufacture for use in Israel or sell appliances unless -

(1)	The Standards Institution or an approved laboratory has tested in accordance with the Standard the electric output of the appliances in standby mode;

(2)	The Superintendent has determined in accordance with the results of the tests according to Paragraph (1) that the electrical output of the appliances in standby mode does not exceed the maximum electrical output stipulated in the Second Addendum.

First Addendum

(Regulation 1)

List of Appliances

Domestic appliances with an electronic display: washing machines, drying machines, dish washers, baking ovens, microwave ovens;

Information technology equipment: computers, computer screens and printers;

Audio equipment: radio sets, amplifiers and wireless telephone sets;

Television receivers, digital decoders for reception of cable and satellite transmissions (except digital converters that are managed by a broadcasting center or through broadcast encryption).

Second Addendum

(Regulation 2)

Maximum electrical output in standby mode of appliances

Appliances in standby mode that return 	Appliances with an electronic display for

to full operation by remote control 	   information on the appliance’s operating mode

or other measures	including clocks

Electric output in standby mode (watt) - 1	Electric output in standby mode (watt) - 2

2nd of 2nd Adar 5771 (March 8, 2011)	Uzi Landau

The Minister of National Infrastructures

# Footnotes

* Published in Regulation Compendium 5771 no. 6989 of March 30, 2011, p. 871.

Errata in Regulation Compendium 5741 no. 7003 dated June 1, 2011, p. 1024.

# Text boxes

Definitions

Duty to comply with maximum electrical output in standby mode

Transfer of information to  the Commissioner

Effect

Transitional instructions

Errata 5771 2011